## Slide 1: PWM Control Box
EPIC Robotz
Nov 2023

## Slide 2: Purpose
Provide a way to manually control TALON based motors for prototyping.
Features
Super Simple to Use
  Simply hook up CAN wires, turn it on, twist a knob.
Self Contained AA Batteries
  that should last for over 50 hours of operation
Battery Monitor
  Power LED blinks when batteries are weak
Direction LEDs confirm output

## Slide 3: Usage Instructions
Pwm Output:
Connect Left to Yellow and
Right to Green
Power LED. Blinks when batteries are weak.
Forward Direction LED. Blinks when slow, and
turns to solid on for high speed.
Control Knob. Center is for motor neutral (“OFF”).
Turn left for reverse and right for forward.
There is a 10% deadband for neutral near the center.
Neutral is indicated by BOTH Direction LEDs being on.
Reverse Direction LED. Blinks when slow, and
turns to solid on for high speed.
On/Off switch. Turn off to save batteries.

## Slide 4: Replacing Batteries
Loosing the two #4 screws
to remove battery cover.
Remove old batteries and insert new
ones in the orientation shown.
Putting batteries in backwards WILL burn
out the microprocessor! Use the orientation shown.

## Slide 5: Schematic

## Slide 6: CAD Files
CAD files located in PDM Valut
Project: F23-CB

## Slide 7: Bill of Materials

## Slide 8: Software
Written in MicroPython
Source Code Located on Github: https://github.com/VCHSRobots/PwmControlBox
Firmware Image for Python on Raspberry Pi: RPI_PICO-20231005-v1.21.0.uf2